## Slide 1
Mini-Project Approval
Project Title : DROWSINESS DETECTION SYSTEM
Project Guide : PROF RAMA DEVI
Project Team : ( Suryanarayan N, PES1201700094
Dheeraj D Gharde, PES1201700075)

## Slide 2
Problem Statement
Drowsiness Detection
With a single inward facing camera, identify drowsiness based on
visual cues like eye closure, yawning, head-nodding and so on. The uphill task is to NOT use any other sensor apart from camera, and using the camera for monitoring the driver for fatigue.

## Slide 3
Literature Survey
List the papers/references studied
  Explain the papers/references
  List their shortcomings which made you think of this new solution
  At the least 3-4 papers/references/competitors need to be studied and presented

## Slide 4
At first we would like to locate the eyes of the driver and make sure to fix on eye aspects so that blink detection is made easier
  Track them for the first 20 mins to collect it in a dataset as eyes vary per person and chances of someone feeling drowsy is extremely rare during this period
  Later we can start testing the live footage with our collected dataset and using machine algorithms and optimising them, we can improve accuracy of the detection
  If permitted to use an infrared sensor and an Arduino, it’ll help us in giving a clear image during nightime and drivers do tend to be more drowsy at that time
Proposed Solution

## Slide 5
Technologies / Methodologies
List
  TensorFlow and OpenCV library file in python will be suited and sufficient for this project as both the machine learning and computer vision aspect can be solved using their functions
  dlib python library

## Slide 6
Technologies / Methodologies
  EAR(Eye Aspect Ratio)
  Unlike traditional image processing methods for computing blinks which typically involve
  Thresholding to find the whites of the eyes.
  Determining if the “white” region of the eyes disappears for a period of time (indicating a blink).
  We are using EAR to detect the blinking, it is just a simple mathematical equation and is faster to compute, it is close to zero when the eyes are closed.
  The dlib library converts the face to an indexable list which make sit easier to access the eye regions.

## Slide 7
Technologies / Methodologies
Video capturing: Video frames from a fixed camera or a smartphone are broken down into a series of images. The video frames are taken in such a manner that only the face of the driver is captured.
Face Detection: The second stage typically aims to detect the face in the image frames. Viola and Jones is the most used algorithm to detect the driver’s face from the image.
However, when CNNs are used, the whole image is typically fed to a network that have multiple filters and features are automatically extracted. CNNs combine the two stages of
detecting the face and feature extraction.
Feature Extraction: If face detection is applied, features are usually extracted using different methods such as landmark localization, Histogram of oriented gradients (HOG), and
Local Binary Patterns (LBP).
Feature Analysis: Extracted features can then be processed further, as is the case for PERCLOS or EAR for eye analysis or mouth-based methods for yawning detection.
Classification: The classification stage consists of classifiers that are used for decision-making on the level of drowsiness in a driver. If the classifier detects traits of drowsiness based on the weighted parameters, then an alarm will be activated suggesting that a driver takes a break.

## Slide 8
Project Timelines & Plan
Provide
  The timelines for execution of the project
  The plan in terms of efforts by individuals in the team.
  We will be following the timelines with respect to the three phases allotted for progress check.
  One of us will be more oriented towards Computer Vision and the other will be optimising the Machine Learning Algorithms.

## Slide 9
Any other information

## Slide 10
Thank You